## Slide 1: Ping Flooding Prevention
ONOS Hackthon Report
Group-2

## Slide 2: Outline
Requirement Analysis
Design Discussion
Implementation

## Slide 3: One Ping APP
Host1 first time ping host2 could pass, but the second or more time ping is dropped within 60s. And in the next 60s, another first ping is allowed, and second or more time ping is forbidden.
One Ping App
ONOS Controller
Device 1
Device 2
Device 3
Host 1
Host 2

## Slide 4: Requirement Analysis
mitigate the impact to the network for unnecessarily frequent or malicious pings
Design goals
  Fulfill the basic functionality
    One-ping-pass for each 60s interval
  Reduce resource consumption
    Avoid unnecessary packet exchange between controller-switch
  Extend to more realistic usage scenarios
    Multi-host, multi-switch

## Slide 5: Outline
Requirement Analysis
Design Discussion
Implementation

## Slide 6: Basic Design
Initialization
For each received packet, loop
  Differentiate 1st ping and other pings
  Allow 1st ping and block other pings
  Clean up at the end of 60s interval
The question:
  Need controller to do the differentiation
Start
Initialization
Ping Differentiation
Ping Handling
End

## Slide 7: Solicit pings to controller: Adding 1st Flow Entry
Initialization
  By default, each ping to packetin to controller. Controller installs the default 1st Flow Entry to all the Switches
For each received packet, loop
  Differentiate 1st ping and other pings
    Controller to identify the 1st ping from the other pings
  Allow 1st ping and block other pings
    Controller to block all the other pings
  Clean up at the end of 60s interval
The next question:
  How to do the differentiation?
Start
Initialization
Install packet-in FE
Ping Differentiation
Ping handling: pass/block
End

## Slide 8: Differentiate 1st ping from the others: Adding first_flag
Initialization
  Set first_flag=1
  By default, each ping to packetin to controller Controller installs the default 1st Flow Entry to all the Switches
For each received packet, loop
  For each packet received
    Check the value of first_flag and differentiate 1st ping from successors
    update first_flag accordingly
  Pass 1st ping and block other pings
  Clean up
    Reset first_flag=1
The next question:
  Wasted resource for pings to be dropped at controller?
Start
Initialization
Install packet-in FE
Set first_flag=1
Ping Differentiation
Check first_flag?=1
Ping Handling
Set first_flag=0
End

## Slide 9: Issue #1: Each ping goes up to controller, consuming bandwidth between centralized controller and switches
One Ping App
ONOS Controller
Device 1
Device 3
Host 1
Host 2
Device 2
…..
ICMP*N
Packet_in*N
ONOS Controller
Device
ICMP Packet-in again
Install Drop FE
Proposed Solution
Life span of 60s
FE expires
Notes: 不配置下发Drop操作流表也可以实现OnePing的功能，但会造成大量的Packet_in报文，与节省网络资源的目的不符

## Slide 10: Adding 2nd Flow Entry
Initialization
  By default, each ping to packetin to controller Controller installs the default 1st Flow Entry to all the Switches
For each received packet, loop
  Differentiate 1st ping and other pings
    Controller to identify the 1st ping from the other pings
  Allow 1st ping and block other pings
    1st ping: pass down to next switch
    Other pings: block
    2nd Flow Entry: Drop for the next 60s all the pings from the source
  Clean up
    Remove 2nd Flow Entry at the end of 60s
The next question:
  What if pings are sent very frequent so that a second ping arrives before the installation and activation of the dropping FE accomplishes in the targeted switch?
Start
Initialization
Install packet-in FE
Set first_flag=1
Ping Differentiation
Check first_flag?=1
Ping Handling
Set first_flag=0
Install drop FE
End

## Slide 11: Issue #2: Controller needs to be prepared for consecutive packet-in pings before the dropping FE reaches the switch and become effective.
ONOS Controller
Device
ICMP Packet_1
ICMP Packet_2
Install Dropping FE
Problem Illustration
Solution
Non-first Ping?
End
Install FE, drop subsequent ICMP packets from Host1
N
Y
Set first_flag=0 in 60s.
Drop
Set first_flag=1
Start
End
Notes: 在连续报文这种极端情况下的处理解决方案 （当执行Drop动作的流表下发至Device前，控制器已经收到了两个或多个控制器报文）

## Slide 12: Handling Rushing-in Pings
Initialization
  By default, each ping to packet-in to controller Controller installs the default 1st Flow Entry to all the Switches
For each received packet, loop
  Differentiate 1st ping and other pings
    Controller to identify the 1st ping from the other pings
  Allow 1st ping and block other pings
    1st ping: pass down to next switch
    Other pings: block
    2nd Flow Entry: Drop for the next 60s all the pings from the source
  Clean up
    Remove 2nd Flow Entry at the end of 60s
The next question:
  Can we support regulation for multiple hosts?
Start
Initialization
Install packet-in FE
Set first_flag=1
Ping Differentiation
Check first_flag?=1
Ping Handling
Set first_flag=0
Install drop FE
Drop other pings
End

## Slide 13: Handling Multiple Hosts
One Ping App
ONOS Controller
Device 1
Device 2
Device 3
Host 1
Host 3
Host 2
Host 4
M
。。。
N
。。。
Replace the bool flag with a recorded list for each src_mac, dst_mac pairs
Use it to check if the ping packet is the 1st ping or not
maintain a checklist for pinged (src_mac, dst_mac) pairs

## Slide 14: Handling Multiple Hosts
Add an entry for the (src_mac, dst_mac) to the record_list.
Flush the list every 60s
Initialization
  By default, each ping to packetin to controller Controller installs the default 1st Flow Entry to all the Switches
  Set record_list = null
For each received packet, loop
  Differentiate 1st ping and other pings
    Controller to identify the 1st ping from the other pings
  Allow 1st ping and block other pings
    1st ping: pass down to next switch
    check the record_list for 1st pings, add it to the list if not present 2nd Flow Entry: Drop for the next 60s all the pings from the source and target macs
  Clean up
    Remove 2nd Flow Entry at the end of 60s
    Flush the record_list at the end of 60s
Acquire the Src_Mac and Dst_Mac for the arrived ping packet
Check it against the record_list for a match?
Install an dropping FE, for matching packet of the same (src_mac and dst_mac) ICMP packets
N
Y
Check if the received packet is icmp?
End
Drop the packet
Y
End
Start
The next question:
  What if there are multiple switches on the ping path?

## Slide 15: Handling Multiple Switches
Add an entry for the (src_mac, dst_mac, device_id) to the record_list.
Flush the list every 60s
Initialization
  By default, each ping to packetin to controller Controller installs the default 1st Flow Entry to all the Switches
  Set record_list = null
For each received packet, loop
  Differentiate 1st ping and other pings
    Controller to identify the 1st ping from the other pings
  Allow 1st ping and block other pings
    1st ping: pass down to next switch
    check the record_list for 1st pings, add it to the list if not present 2nd Flow Entry: Drop for the next 60s all the pings from the source and target macs
  Clean up
    Remove 2nd Flow Entry at the end of 60s
    Flush the record_list at the end of 60s
Acquire the Src_Mac, Dst_Mac and device_id for the arrviced ping packet
Check it against the record_list for a match?
Install an dropping FE, for matching packet of the same (src_mac and dst_mac, device_id) ICMP packets
N
Y
Check if the received packet is icmp?
End
Drop the packet
Y
End
Start
The next question:
  What if there are multiple switches on the ping path?

## Slide 16
One Ping App
ONOS Controller
Device 1
Device 3
Host 1
Host 2
Device 2
OnePingApp delay measurement path
Original ping delay measurement path
LatencyMeasurePing
Two consecutive FEs for non-first pings
Allow to pass for a short time;
Block afterwards by the end of 60s.
Start
Controller figures out if the packet is 1st ping?
Acquire the Src_Mac, Dst_Mac and device_id for the arrviced ping packet
Check it against the record_list for a match?
End
N
Y
Y
Y
End
Drop the packet.
Pass to next S
End
Add an entry for the (src_mac, dst_mac) to the record_list.
Flush the list every 60s
Install an forwarding FE, for matching packet of the same (src_mac, dst_mac, device_id) ICMP packets for 1s.
Install an dropping FE for 59s.
Notes: Ping功能的作用：1）验证端到端业务路径连通性；2）得到端到端业务路径时延；
OnePingApp解决方案返回的时延是经过控制器的时延（红色线）；
LatencyMeasurePing功能可以实现在减少Ping报文数量的前提下，返回业务路径时延（绿色线）；

## Slide 17: Outline
Requirement Analysis
Design Discussion
Implementation

## Slide 18: Building Blocks for Basic Implementation
Key Classes used
  public interface PacketProcessor; //the main process for packet handling process
  public interface PacketService; //the interface for packet handling
  public interface FlowObjectiveService; //Service Interface for flow objective
Key Functions used
  PacketService related
    void addProcessor(PacketProcessor processor, int priority) // add a new processor to the main function
  FlowObjectiveService related
    void forward(DeviceId Id, ForwardingObjective forwardingObjective) // install the 1st and 2nd flow entry with a life span of 60 seconds

## Slide 19
开始
下发ICMP转发流表1，将ICMP报文上送控制器
控制器判断是否为ICMP报文
获取Src_Mac，Dst_Mac，Device_Id
根据上述参数检查是否被ping过
结束
下发流表，对匹配Src_Mac，Dst_Mac的ICMP报文执行Drop动作
否
否
是
是
将Src_Mac，Dst_Mac，Device_Id作为List加入是否被ping过的筛选模块，并设置生存周期为60s
转到FWD处理模块
结束
中断操作，丢弃报文
转到FWD处理模块
结束
Start
flowObjectiveService.forward
IsIcmp(Ethnet)
ethnet.getSourceMAC;
packetContext.inPacket().receivedFrom().deviceId();
if (hasPinged)
End
flowObjectiveService.forward
Y
N
Y
N
hasPingedHost.add
(srcMac,dstMac,deviceId)
FwdPacketProcess
End
packetContext.block();
FwdPacketProcess
END

## Slide 20
Start
flowObjectiveService.forward
IsIcmp(Ethnet)
ethnet.getSourceMAC;
packetContext.inPacket().receivedFrom().deviceId();
if (hasPinged)
End
flowObjectiveService.forward
Y
N
Y
N
hasPingedHost.add
(srcMac,dstMac,deviceId)
FwdPacketProcess
End
packetContext.block();
FwdPacketProcess
END
Simplifying the tasks for the Controller
Controller might be loaded for the lookups into Record_list
  Multi-keyed
  Hash-mapping
  Resource consuming
  Controller single point of failure
Implementation Compromise
  Eliminate the record_list from controller
  The network might be allowing consecutive pings to pass during a short time period (before the 2nd FE is installed and take effection, but the controller is protected.
More simple, more realistic solution.

## Slide 21: Workaround for Hard-timeout
Hard-timeout is expected to be set with 2nd FE
We assumed that requestPacket() supports hard-timeout
But the reality is
  The forwarding ping request is always passed, while
  The returning ping ack is always blocked
  Something is wrong…
It is idle-time out which is supported
And with No NB API found for setting hard-timeout
We came up with a workaround
Start
Install the 1st FE
Packet-in for ICMP packets
IsICMP?
Acquire Src_Mac，Dst_Mac，Device_Id for the packet
Install 2nd FE, dropping ICMP packets matching (Src_Mac,Dst_Mac)
N
Y
After 60s, install 3rd FE, packet-in ICMP packets matching (Src_mac, Dst_mac)
Forward to FWD
End
Override the 2nd FE
Outdated FE expires naturally and get deleted after idle_timeout.

## Slide 22: Demo Basic Functionality

## Slide 23: Demo 1st FE (Static Packet-in rule in Initialization Phase)

## Slide 24: Demo Core code (FE Coverup Feature)

## Slide 25: Demo Multi-Host and Multi-Device Feature

## Slide 26: Demo Summary
Simplicity: FE cover-up feature
Network-friendly: reduced packet-in messages, reduced bandwidth consumption between controller and switches
Controller-friendly: rely on the data plane to enforce the policy, reduced local computation resource consumption to the controller
Scalability: with a light-weight implementation on the controller side, the system scales better with the number of switches
Notes: 四个优点：
巧妙地利用了流表会cover的特性，选择了简单的实现方法 Simplecity
避免了packet_in的消息数量，减少了带宽的占用
将60s内通ping包的判断策略在数据平面上实现，控制器通过简单的流表策略即可实现，避免了复杂的计算，减轻了控制器的负担
4. 旧方法需要在控制层维护一个HushMap，大的拓扑的时候维护很困难

## Slide 27: Thank you.